UNIT 1.1 Boolean Logic
Boolean Expression
f(x, y, z) = (x AND y) OR (NOT(x) AND z)

Truth table:
x y z f
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 0
1 1 0 1
1 1 1 1

Boolean Identities
Commutative Laws:
- (x AND y) = (y AND x)
- (x OR y) = (y OR x)
Associative Laws:
- (x AND (y AND z)) = ((x AND y) AND z)
- (x OR (x OR z) = ((x OR y) OR z)
Distributive Laws:
- (x AND (y OR z)) = (x AND y) OR (x AND z)
- (x OR (y and z)) = (x OR y) and (x OR z)
De Morgan laws:
- NOT(x AND y) = NOT(x) OR NOT(y)
- NOT (x OR y) = NOT(x) AND NOT(y)

Boolean Algebra:
NOT (NOT(x) AND NOT(x

Truth table to Boolean Expression
Truth table row by row. We construct expressions
at rows where function returns 1 only at the specific rows
and zeroes at other rows and OR them together
x y z f
0 0 0 1 (NOT(x) AND NOT (y) AND NOT(z)) OR
0 0 1 0
0 1 0 1 (NOT(x) AND y AND NOT(z)) OR
0 1 1 0
1 0 0 1 (x AND NOT(y) AND NOT (z))
1 0 1 0
1 1 0 0
1 1 1 0

(NOT(x) AND NOT (y) AND NOT(z)) OR NOT(x) AND y AND NOT(z)) OR (x AND NOT(y) AND NOT (z))

Theorem: Any boolean function can be represented using an expression containing AND, OR and NOT operations

Theorem: Any boolean function can be represented using an expression containing only NAND operations
Proof:
1. NOT(x) = (x NAND x)
2. (x AND y) – NOT(x NAND y)

Gate Logic
Elementary (Nand, And, Or, Not, ...)
Composite (Mux, Adder, ...)

Nand: if (a==1 and b==1) then out=0 else out=1
And: if (a==1 and b==1) then out=1 else out=0
Not: if (in==0) then out=1 else out=0

Abstraction levels:
  - interface is answering the question "What"
  - implementation answers "How"

From gate diagram to HDL (Hardware Description Language)
XOR sample implementation:
/** Xor gate: out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;

PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}

Xor implementation:
XOR truth table:
a b out
0 0 0
0 1 1
1 0 1
1 1 0

so out = 1 when (a And Not(b)) Or (b And Not(a))

HDL is functional/declarative language

Hardware Simulation
HDL code -> interactive hardware simulator or test script

test script:
load xor.hdl,
output-file And.out,
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;

With/without output and compare files

Exercise – implement AND, OR, NOT using only NAND

NAND
a b out
0 0 1
0 1 1
1 0 1
1 1 0

AND
a b out
0 0 0
0 1 0
1 0 0
1 1 1

OR
a b out
0 0 0
0 1 1
1 0 1
1 1 1

NOT:
0 1
1 0

XOR
a b out
0 0 0
0 1 1 Not(a) And b
1 0 1 a And Not(b)
1 1 0

we implement OR using De Morgan Law and double negation law
NOT (x OR y) = NOT(x) AND NOT(y)

Hardware construction projects :
System architects – decide which chips are needed, create API, test script and compare file
Developers – given these resources they build chip

Multi-Bit Buses

CHIP Add3Way16{
IN first[16], second[16], third[16];
OUT out[16];

PARTS:
Add16(a=first, b=second, out=temp);
Add16(a=temp, b=third, out=out);
}

access particular bits in a bus:
 CHIP Add4Way{
IN a[4];
OUT out;

PARTS:
And (a=a[0], b=a[1], out=t01);
And (a=t01, b=a[2], out=t012);
And (a=t012, b=a[3], out=out);
}

CHIP And4 {
IN a[4], b[4];
OUT out[4];

PARTS:
AND(a=a[0], b=b[0], out=out[0];
AND(a=a[1], b=b[1], out=out[1];
AND(a=a[2], b=b[2], out=out[2];
AND(a=a[3], b=b[3], out=out[3];
}

Buses can be composed from a(and broken into) sub-buses:
..
IN lsb[8], msb[8],....
..
Add16(a[0..7], a[8..15]=msb, b=..., out=...);
Add16(.., out[0..3]=t1, out[4..15]=t2);
}

Project 1 Overview
Given: Nand
Goal: Build following gates:
Elementary: Not, And, Or, Xor, Mux, Dmux
 16 Bits variants: Not16, And16, Or16, Mux16
Multi-way variants: Or8Way, Mux4Way16, Mux8Way16,DMux4Way, Dmux8Way

Why these 15 particulare gatres? - They are commonly used gates, they comprise all the elementary logic gates to build out computer

16-bits variants example: And16

Multi-way variants example: 16-bit, 4-way multiplexor

UNIT 2

In a nutshell: Using the chipset that we've built in the previous module, we will now proceed to build a family of adders -- chips designed to add numbers. We will then take a big step forward and build an Arithmetic Logic Unit. The ALU, which is designed to perform a whole set of arithmetic and logical operations, is the computer's calculating brain. Later in the course we will use this ALU as the centerpiece chip from which we will build the computer's Central Processing Unit, or CPU. Since all these chips operate on binary numbers (0's and 1's), we will start this module with a general overview of binary arithmetic, and only then delve into building the ALU.
Key concepts: Binary numbers, binary addition, the two's complement method, half-adders, full-adders, n-bit adders, counters, Arithmetic Logic Unit (ALU), combinational logic.