UNIT 1.1 Boolean Logic
Boolean Expression
f(x, y, z) = (x AND y) OR (NOT(x) AND z)

Truth table:
x y z f
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 0
1 1 0 1
1 1 1 1

Boolean Identities
Commutative Laws:
- (x AND y) = (y AND x)
- (x OR y) = (y OR x)
Associative Laws:
- (x AND (y AND z)) = ((x AND y) AND z)
- (x OR (x OR z) = ((x OR y) OR z)
Distributive Laws:
- (x AND (y OR z)) = (x AND y) OR (x AND z)
- (x OR (y and z)) = (x OR y) and (x OR z)
De Morgan laws:
- NOT(x AND y) = NOT(x) OR NOT(y)
- NOT (x OR y) = NOT(x) AND NOT(y)

Boolean Algebra:
NOT (NOT(x) AND NOT(x

Truth table to Boolean Expression
Truth table row by row. We construct expressions
at rows where function returns 1 only at the specific rows
and zeroes at other rows and OR them together
x y z f
0 0 0 1 (NOT(x) AND NOT (y) AND NOT(z)) OR
0 0 1 0
0 1 0 1 (NOT(x) AND y AND NOT(z)) OR
0 1 1 0
1 0 0 1 (x AND NOT(y) AND NOT (z))
1 0 1 0
1 1 0 0
1 1 1 0

(NOT(x) AND NOT (y) AND NOT(z)) OR NOT(x) AND y AND NOT(z)) OR (x AND NOT(y) AND NOT (z))

Theorem: Any boolean function can be represented using an expression containing AND, OR and NOT operations

Theorem: Any boolean function can be represented using an expression containing only NAND operations
Proof:
1. NOT(x) = (x NAND x)
2. (x AND y) – NOT(x NAND y)

Gate Logic
Elementary (Nand, And, Or, Not, ...)
Composite (Mux, Adder, ...)

Nand: if (a==1 and b==1) then out=0 else out=1
And: if (a==1 and b==1) then out=1 else out=0
Not: if (in==0) then out=1 else out=0

Abstraction levels:
  - interface is answering the question "What"
  - implementation answers "How"

From gate diagram to HDL (Hardware Description Language)
XOR sample implementation:
/** Xor gate: out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;

PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}

Xor implementation:
XOR truth table:
a b out
0 0 0
0 1 1
1 0 1
1 1 0

so out = 1 when (a And Not(b)) Or (b And Not(a))

HDL is functional/declarative language

Hardware Simulation
HDL code -> interactive hardware simulator or test script

test script:
load xor.hdl,
output-file And.out,
output-list a b out;
set a 0, set b 0, eval, output;
set a 0, set b 1, eval, output;
set a 1, set b 0, eval, output;
set a 1, set b 1, eval, output;

With/without output and compare files

Exercise – implement AND, OR, NOT using only NAND

NAND
a b out
0 0 1
0 1 1
1 0 1
1 1 0

AND
a b out
0 0 0
0 1 0
1	0
1 1 1

OR
a b out
0 0 0
0 1 1
1 0 1
1 1 1

NOT:
0 1
1 0

XOR
a b out
0 0 0
0 1 1 Not(a) And b
1 0 1 a And Not(b)
1 1 0

we implement OR using De Morgan Law and double negation law
NOT (x OR y) = NOT(x) AND NOT(y)

Hardware construction projects :
System architects – decide which chips are needed, create API, test script and compare file
Developers – given these resources they build chip

Multi-Bit Buses

CHIP Add3Way16{
IN first[16], second[16], third[16];
OUT out[16];

PARTS:
Add16(a=first, b=second, out=temp);
Add16(a=temp, b=third, out=out);
}

access particular bits in a bus:
 CHIP Add4Way{
IN a[4];
OUT out;

PARTS:
And (a=a[0], b=a[1], out=t01);
And (a=t01, b=a[2], out=t012);
And (a=t012, b=a[3], out=out);
}

CHIP And4 {
IN a[4], b[4];
OUT out[4];

PARTS:
AND(a=a[0], b=b[0], out=out[0];
AND(a=a[1], b=b[1], out=out[1];
AND(a=a[2], b=b[2], out=out[2];
AND(a=a[3], b=b[3], out=out[3];
}

Buses can be composed from a(and broken into) sub-buses:
..
IN lsb[8], msb[8],....
..
Add16(a[0..7], a[8..15]=msb, b=..., out=...);
Add16(.., out[0..3]=t1, out[4..15]=t2);
}

Project 1 Overview
Given: Nand
Goal: Build following gates:
Elementary: Not, And, Or, Xor, Mux, Dmux
 16 Bits variants: Not16, And16, Or16, Mux16
Multi-way variants: Or8Way, Mux4Way16, Mux8Way16,DMux4Way, Dmux8Way

Why these 15 particulare gatres? - They are commonly used gates, they comprise all the elementary logic gates to build out computer

16-bits variants example: And16

Multi-way variants example: 16-bit, 4-way multiplexor

UNIT 2

In a nutshell: Using the chipset that we've built in the previous module, we will now proceed to build a family of adders -- chips designed to add numbers. We will then take a big step forward and build an Arithmetic Logic Unit. The ALU, which is designed to perform a whole set of arithmetic and logical operations, is the computer's calculating brain. Later in the course we will use this ALU as the centerpiece chip from which we will build the computer's Central Processing Unit, or CPU. Since all these chips operate on binary numbers (0's and 1's), we will start this module with a general overview of binary arithmetic, and only then delve into building the ALU.
Key concepts: Binary numbers, binary addition, the two's complement method, half-adders, full-adders, n-bit adders, counters, Arithmetic Logic Unit (ALU), combinational logic.

Unit 2.1: Binary Numbers

With 8 bits we can represent 2^8-1 = 255 values or -128 to 127

binary to decimal: 99 = 64 + 32 + 2 +1 = 0100 0011

Unit 2.1 Binary Addition
00010101 +
01011100
------------
01110001

01111101 +
00110110
-----------
10110011

Building an Adder
1. Half Adder – adds two bits
2. Full Adder – adds three bits
3. Adders – Add two numbers

Half Adder – truth table
a b sum carry
0 0 0 0
0 1 1 0
1 0 1 0
1 1 0 1

Full Adder – truth table
a b c sum carry
0 0 0 0 0
0 0 1 1 0
0 1 0 1 0
0 1 1 0 1
1 0 0 1 0
1 0 1 0 1
1 1 0 0 1
1 1 1 1 1

Multi-bit Adder

Unit 2.3 Negative Numbers

If 6 is 0110 how much is -6:

Unit 2.5 Arithmetic Logic Unit – ALU
Von Neumann Architecture – 1945

The Hack ALU
Specification:

Project 2 Overview
Given: All the chips built in Project 1
Goal: Build HalfAdder, FullAdder, Add16, Inc16, ALU

Project 3 – RAM and Counter

Project 4 – optional - assembly

Assembler features:
  - Working with registers and memory
  - Branching
  - Variables
  - Iteration
  - Pointers
  - Input / output

Registers:
 D: data register
A: address/data register
M: currently selected memory register M = RAM[A]

//D=10 – can't be done directly so:
@10
D=A

//D++
D=D+1

// D=RAM[17]
@17
D=M

//RAM[17]=D
@17
M=D

//RAM[17]=0
@17
M=0

//RAM[17]=10
@10
D=A
@17
M=D

//RAM[5] = RAM[3]
@3
D=M
@5
M=D

//Program Add2.asm
//Computer RAM[2] = RAM[0] + RAM[1]
@0
D=M
@1
D=D+M
@2
M=D

We should terminate the program propertly:
@6
0;JMP
Best practise: end the program with infinite loop

Built-in symbols: /assembler replaces symbol name with its value/
Symbol	Value
R0..R15	0..15	//virtual registers
SCREEN	16384
KBD	24576

SP	0
LCL	1
ARG	2
THIS	3
THAT	4

Why do we need symbols?
//we want to put 15 into RAM[5]
// RAM[5]=15
@15 //we use register A to store value – the constant 15
D=A
@5 //we use regiser A to address desired memory where we will store the constant
M=D

variant 2:
//
@15
D=A
@R5 // its clear that the programmer wants to address RAM[5]
M=D

Branching – ability to tell the computer to evaluate condition and based on the result to continue with next instruction or jump to another instruction

// Program Signum.asm
// Computes: if R0>0
//	R1=1
//	else R1=0
@R0
D=M
@8
D;JGT
@0
D=A
@10
0;JMP
@1
D=A
@R1
M=D

Symbolic references (Labels):
// Program Signum.asm
// Computes: if R0>0
//	R1=1
//	else R1=0
@R0
D=M
@POSITIVE
D;JGT
@0
D=A
@END
0;JMP
(POSITIVE)
@1
D=A
(END)
@R1
M=D

@LABEL translates to @n, where n is the instruction number following the (LABEL) declaration

Variables – abstraction of a container that has name and value
We will use a single register to represent a variable
// Program: Flip.asm – flips the values of RAM[0] and RAM[1]
// temp = R1
// R1 = R0
// R0 = temp

@R1
D=M
@temp // we declare variable to hold value of RAM[0]
M=D // temp = R1

@R0
D=M
@R1
M=D // R1 = R0

@temp
D=M
@R0
M=D

(END)
@END
0; JMP

@temp: “find some available memory register (say register n), and use it to represent variable temp. Som from now on, each occurrence of @temp in the program will be translated into @n”

A reference to a symbol that has no corresponding label declaration is treated as a reference to a variable.

Variables are allocated to the RAM from address 16 onward

The program is relocatable – you can load it anywhere in the memory and you just have to know its “base” address

Iterative processing
Example: Compute 1 + 2 + … + n
// Computes RAM[1] = 1 + 2 + RAM[0]
// n = RAM[0]
// sum = 0
// i=1
// LOOP:
// if i > n goto STOP
// sum = sum + i
// i = i + 1
// goto loop
STOP:
R1 = SUM

// sum.asm
@0 // sum = 0
D=M
@sum
M=D

@1 // i = 1
D=M
@i
M=D

@R0 // n = 0
D=M
@n
M=D

(LOOP)
@n
D=M
@i
D=D-M
@STOP
D; JLT
@i
M=M+1
goto LOOP
(STOP)
@sum
D=M
@R1
M=D

Pointers – TODO video Unit 4.8 00:04:00 write example source code!
The notion of array is lost when code is translated to assembler
In machine language we know the base address and length of an array

Variables that store memory addresses, like arr and i, are called pointers

Hack pointer logic: whenever we have to access memory using a pointer, we need an instruction like A=M

Typical pointer semantics : “set the address register to the contents of some memory register”
Example:
// for (i=0; i<n; i++) {
//	arr[i] = -1 }
// suppose that arr=100 and n=10
@100 // arr = 100
D=A
@arr
M=D

Input/output
Memory map:
0-16383 data memory (16K)
16384 – 24575 screen (8K - 512x256)
24576 - keyboard

Exercise 1: draw a filled rectangle at the upper left corner of the screen, 16 points wide and RAM[0] point high

pseudo code:
// for (i=0; i<n; i++)
// { draw 16 black pixels at the beginning of row i }
//

// rectangle.asm – draws a rectangle at the top left of the screen

End note: compilation
High level code:
//for (i=0; i<n; i++) { arr[i] = -1 }

Assembly:
@i
M=0
(LOOP)
@i
D=M
@n
D=D-M
@END
D;JEQ
@arr
D=M
@i
A=D+M //pointer arithmetic A= arr + i
M=-1
@i
M=M+1
@LOOP
0; JMP
(END)
@END
0; JMP

Project 4 Overview
task 1:
// a program performing R2 = R0 * R1
// use simplest solution

task2:
// simple interactive program: listen to the keyboard, and once user touch
// a key the program blackens the screen completely until user releases the key
// tip use infinite loop

//
// task 1 pseudo code R2 = R0 * R1
// multiplier = R1
// i=0
//result = R0
// (LOOP)
// if i=multiplier goto end
// result = result + R0

@0
D=A
@i
M=D // init i=0;

@R1
D=M
@multiplier
M=D // multiplier = R1
@0
D=A
@result
M=D // init result=0
(LOOP)
@multiplier
D=M
@i
D=D-M
@END
D; JEQ // if i==multiplier exit loop
@R0
D=M
@result
M=D+M
@i
M=M+1
@LOOP
0; JMP
(END)
@END
0; JMP

// task2
//
//read kbd
// if !=0 black screen
//
//(FILL BLACK)

Project 5

ALU: